## Slide 1: Data Communication and Computer Networks
First Semester 2011/2012
Sana Ahmed
Notes: <number>

## Slide 2: Data Communication
<number>
Data Communications are the exchange of data between two devices via some form of transmission.
Notes: <number>

## Slide 3: Data Communication Characteristics
<number>
1. Delivery:
The system must deliver data to the correct destination.
2. Accuracy:
The system must deliver data accurately.
3. Timelines:
The system must deliver data in timely manner.
4. Jitter: refers to the variation in the packet arrival time
Notes: <number>

## Slide 4: Components of Data Communication
<number>
Receiver
Sender
Message
Protocol
Rules
.
.
.
Rules
.
.
.
Protocol
Notes: <number>

## Slide 5: Components of Data Communication cont.
<number>
1. Message:
information
2. Sender:
The device that send the msg.
3. Receiver:
The device that receive the msg.
4. Transmission Medium:
The physical path between sender and receiver ,the message travel
5. Protocol:
A set of rules that govern data communication.
Notes: <number>

## Slide 6: Data Flow in Communication
<number>
Simplex: one direction only
Half-duplex: two-way alternate
In different time
Notes: <number>

## Slide 7: Data Flow in Communication cont.
<number>
Duplex: two-way concurrent .
At same time
Notes: <number>

## Slide 8: Network
<number>
A Network is a set of node connected together by communication link to share resources and to transmit information.
Node : Computer, Printer, Scanner, Software, etc.
Information: text, voice, picture, etc
Notes: <number>

## Slide 9
<number>
Why Network ?????
Sharing
Sharing of What ?????
Resources
What Resources ?????
Printer, Scanner, Memory, Information
Network Bandwidth, Internet Services, Data Base, etc.
Notes: <number>

## Slide 10: Network Services
<number>
Sharing (file, printer, application).
Internet browsing.
Fax Service.
Telephony.
Conferencing.
Database.
Backup.
Notes: <number>

## Slide 11: Network Components
<number>
Cables (wired, wireless ).
Network Operating System (NOS).
Network Interface Card (NIC).
Network Hardware:-
Hubs.
Switches.
Routers.
Gateways.
Access Point.
Repeaters.
Notes: <number>

## Slide 12: Network Interface Card
<number>
Notes: <number>

## Slide 13: Network Classification
<number>
Upon the transmission medium( type of connection ):-
1. Point-to-point:
2. Multipoint:
Notes: <number>

## Slide 14: Point-to-Point
<number>
A pair of nodes connected together via dedicated link.
Point-to-point between television and remote control via IR (infrared)
PC
PC
Link
Remote control
IR
Television
Notes: <number>

## Slide 15: Multipoint
<number>
Number of node connected and share a single link.
Mainframe
PC
PC
PC
Link
Notes: <number>

## Slide 16: Network Classification
<number>
Upon the scale (size):-
PAN (Personal Area Network).
LAN (Local Area Network).
CAN (Campus Area Network).
MAN (Metropolitan Area Network).
WAN (Wide Area Network).
Notes: <number>

## Slide 17: PAN (Personal Area Network)
<number>
PAN is a short-distance network design to individual user (person).
PAN may be contain:- printer, mobile, computer, wireless printers , PDA, etc.
components of PAN connected together via Bluetooth , USB cable ,IrDA (infrared), etc.
Notes: <number>

## Slide 18: PAN cont.
<number>
Wireless Printer
Bluetooth
IrDA
PDA
USB Cable
Scanner
Notes: <number>

## Slide 19: LAN (Local Area Network)
<number>
A LAN is a group of node connected together in a small specific area.
LAN may be contain workstations, computers, scanner, printers, servers, etc.
Notes: <number>

## Slide 20: LAN cont.
<number>
………..
…….………..
Floor 1
Floor 2
Floor 3
Floor 4
Notes: <number>

## Slide 21: CAN (Campus Area Network)
<number>
A CAN is a group of interconnection LAN within limited geographical area.
A CAN using in school campus, military base, university campus ,etc.
Notes: <number>

## Slide 22: CAN cont.
<number>
Administration building
University library
IT faculty
Notes: <number>

## Slide 23: MAN (Metropolitan Area Network)
<number>
A MAN is a large computer network uses to connect between LAN in different location (cities).
A MAN is a group of node connect together over city.
Notes: <number>

## Slide 24: MAN cont.
<number>
LAN 1
LAN 4
LAN 3
LAN 2
Connect different branch location in city
Notes: <number>

## Slide 25: WAN (Wide Area Network)
<number>
A WAN is a computer network that covers large geographical area.
WANs are used to connect types of networks together.
Notes: <number>

## Slide 26: WAN cont.
<number>
Notes: <number>

## Slide 27
<number>
WAN
MAN
CAN
LAN
PAN
Notes: <number>

## Slide 28: Network Criteria
<number>
Performance:
The performance of network depends on a number of factors
The performance is evaluate by two networking metric : Throughput and Delay.
Reliability:
The network reliability is measured by the frequency of failure, (the time it takes a link to recover from of failure).
Notes: <number>

## Slide 29: Network Criteria cont.
<number>
Security:
Network security include protecting data from unauthorized access, protecting data from damage, and write policies and implementing it for security issues.
Notes: <number>

## Slide 30: Network Modes
<number>
Unicast Mode:
Single source send to single node.
one-to-one
Notes: <number>

## Slide 31: Broadcast Mode
<number>
Single source send to all others node that are connected to same Network
one-to-all
Notes: <number>

## Slide 32: Multicast Mode
<number>
Single source send to specific nodes (group) that are connected to same Network.
one-to-many
Notes: <number>

## Slide 33: Physical Topology
<number>
Determines how the network nodes are connected together.
Bus Topology
Star Topology
Ring Topology
Mesh Topology
Notes: <number>