## Slide 1: INTRODUCTION TO COMPUTER NETWORKS
Introduction to Computer Networks
SANA AHMED
FOURTH GRAD
(4)
Notes: <number>

## Slide 2
<number>
Dotted-decimal notation:
IPv4 uses 32-bit addresses
Each connection has a unique address
The address space is 2^32 = 4,294,967,296
IP Addresses: Classful Addressing

## Slide 3
<number>
Change the following IP addresses from binary notation to dotted-decimal notation.
a. 10000001 00001011 00001011 11101111 b. 11000001 10000011 00011011 11111111 c. 11100111 11011011 10001011 01101111 d. 11111001 10011011 11111011 00001111
Example 1
Solution We replace each group of 8 bits with its equivalent decimal number (see Appendix B) and add dots for separation:
a. 129.11.11.239 b. 193.131.27.255 c. 231.219.139.111 d. 249.155.251.15

## Slide 4
<number>
Change the following IP addresses from dotted-decimal notation to binary notation.
a. 111.56.45.78 b. 221.34.7.82 c. 241.8.56.12 d. 75.45.34.78
Example 2
Solution
We replace each decimal number with its binary equivalent:
a. 01101111 00111000 00101101 01001110 b. 11011101 00100010 00000111 01010010 c. 11110001 00001000 00111000 00001100 d. 01001011 00101101 00100010 01001110

## Slide 5
<number>
Change the following IP addresses from binary notation to hexadecimal notation.
a. 10000001 00001011 00001011 11101111
b. 11000001 10000011 00011011 11111111
Example 4
Solution We replace each group of 4 bits with its hexadecimal equivalent (see Appendix B). Note that hexadecimal notation normally has no added spaces or dots; however, 0X (or 0x) is added at the beginning or the subscript 16 at the end to show that the number is in hexadecimal.
a. 0X810B0BEF or 810B0BEF16 b. 0XC1831BFF or C1831BFF16

## Slide 6
<number>
4.2 CLASSFUL ADDRESSING
IP addresses, when started a few decades ago, used the concept of classes. This architecture is called classful addressing. In the mid-1990s, a new architecture, called classless addressing, was introduced and will eventually supersede the original architecture. However, part of the Internet is still using classful addressing, but the migration is very fast.
The topics discussed in this section include:
Recognizing Classes
Netid and Hostid
Classes and Blocks
Network Addresses
Sufficient Information
Mask
CIDR Notation
Address Depletion

## Slide 7
<number>
Occupation of the address space
Class A addresses cover ½ the address space!!
Millions of class A addresses are wasted!
Table 4.1 Addresses per class

## Slide 8
<number>
Finding the class in binary notation

## Slide 9
<number>
Find the class of each address:
a. 00000001 00001011 00001011 11101111 b. 11000001 10000011 00011011 11111111 c. 10100111 11011011 10001011 01101111 d. 11110011 10011011 11111011 00001111
Example 6
Solution See the procedure in Figure 4.4. a. The first bit is 0. This is a class A address. b. The first 2 bits are 1; the third bit is 0. This is a class C address. c. The first bit is 0; the second bit is 1. This is a class B address. d. The first 4 bits are 1s. This is a class E address..

## Slide 10
<number>
Finding the class in decimal notation

## Slide 11
<number>
Find the class of each address:
a. 227.12.14.87 b.193.14.56.22 c.14.23.120.8 d. 252.5.15.111 e.134.11.78.56
Example 7
Solution a. The first byte is 227 (between 224 and 239); the class is D. b. The first byte is 193 (between 192 and 223); the class is C. c. The first byte is 14 (between 0 and 127); the class is A. d. The first byte is 252 (between 240 and 255); the class is E. e. The first byte is 134 (between 128 and 191); the class is B.

## Slide 12
<number>
Figure 4.6 Netid and hostid
Class A, B and C addresses are divided into 2 parts: Netid and
Hostid.

## Slide 13
<number>
Blocks in class A

## Slide 14
<number>
Blocks in class B
Many class B addresses are wasted too.

## Slide 15
<number>
Figure 4.9 Blocks in class C
Class C blocks are too small for most businesses.

## Slide 16
<number>
In classful addressing, the network address (the first address in the block) is the one that is assigned to the organization. The range of addresses can automatically be inferred from the network address.
Note:

## Slide 17
<number>
Given the network address 17.0.0.0, find the class, the block, and the range of the addresses.
Example 9
Solution The class is A because the first byte is between 0 and 127. The block has a netid of 17. The addresses range from 17.0.0.0 to 17.255.255.255.

## Slide 18: Example 10
<number>
Given the network address 132.21.0.0, find the class, the block, and the range of addresses.
The class is B, the block is 132.21, and the range is 132.21.0.0 to 132.21.255.255

## Slide 19: Example 11
<number>
Given the network address 220.34.76.0, find the class, the block, and the range of addresses
The class is C, the block is 220.34.76, and the range of addresses is 220.34.76.0 to 220.34.76.255

## Slide 20
<number>
Masking concept
Given an address from a block of addresses, we can find
the network address by ANDing with a mask.

## Slide 21
<number>
Table 4.2 Default masks

## Slide 22
<number>
The network address is the beginning address of each block. It can be found by applying the default mask to any of the addresses in the block (including itself). It retains the netid of the block and sets the hostid to zero.
Note:

## Slide 23
<number>
Given the address 23.56.7.91, find the beginning address (network address) and default mask.
Example 12
Solution The default mask is 255.0.0.0, which means that only the first byte is preserved and the other 3 bytes are set to 0s. The network address is 23.0.0.0.

## Slide 24
<number>
Given the address 132.6.17.85, find the beginning address (network address) and default mask.
Example 13
Solution The default mask is 255.255.0.0, which means that the first 2 bytes are preserved and the other 2 bytes are set to 0s. The network address is 132.6.0.0.

## Slide 25
<number>
Given the address 201.180.56.5, find the beginning address (network address).
Example 14
Solution The default mask is 255.255.255.0, which means that the first 3 bytes are preserved and the last byte is set to 0. The network address is 201.180.56.0.

## Slide 26
<number>
Note that we must not apply the default mask of one class to an address belonging to another class.
Note:

## Slide 27
<number>
4.3 OTHER ISSUES
In this section, we discuss some other issues that are related to addressing in general and classful addressing in particular.
The topics discussed in this section include:
Multihomed Devices
Location, Not Names
Special Addresses
Private Addresses
Unicast, Multicast, and Broadcast Addresses

## Slide 28
<number>
Figure 4.12 Multihomed devices
A computer that is connected to different networks is called a
multihomed computer and will have more than one address, each
possibly belonging to a different class. Routers are multihomed too.
Recall- an IP address identifies a connection, not a device.

## Slide 29
<number>
Table 4.3 Special addresses

## Slide 30
<number>
Network address

## Slide 31
<number>
Example of direct broadcast address

## Slide 32
<number>
Example of limited broadcast address

## Slide 33
<number>
Figure 4.16 Examples of “this host on this network”
Example: starting a dial-up connection with DHCP.

## Slide 34
<number>
Figure 4.17 Example of “specific host on this network”

## Slide 35
<number>
Figure 4.18 Example of loopback address
This address used to test the software. Packet never leaves the
machine. A client process can send a message to a server process
on the same machine.

## Slide 36
<number>
Sample internet