## Slide 1: INTRODUCTION TO COMPUTER NETWORKS
Introduction to Computer Networks
SANA AHMED
FOURTH GRAD
(5)
Notes: <number>

## Slide 2: IP Addressing
<number>
Notes: <number>
Layer 3 of 3
Emphasize: In layer 3, an example of dotted decimal format and binary are displayed.
IP address format is dotted decimal. Dotted decimal makes it easy to work with IP addresses. However, in this course we will work with the addresses on the bit level, so we will convert these addresses into binary, make changes to them, and convert them back.
The central authority for addresses is the Internet Assigned Numbers Authority (IANA).
Note: This most common form of addressing reflects the widely used IP version 4. Faced with the problem of depleting available addresses, Internet Engineering Task Force (IETF) work is under way for a backward-compatible next generation of IP (IPng, also called IP 6).
IP 6 will offer expanded routing and addressing capabilities with 128-bit addresses rather than the 32-bit addressing shown on the graphic. Addresses from both IP versions will coexist. Initial occurrences will probably be at locations with address translator software and firewalls.

## Slide 3: IP Address Classes
<number>
Notes: <number>
Slide 2 of 2
Emphasize: Highlight the fixed values that start each class address.
The first octet rule states that when an address falls into a specified range, it belongs to a certain class. Students should soon be able to recognize the address class of any IP address on sight.
Note: If time or interest permits, you can use the initial bit patterns in the first octet and show how a class of IP network derives the range of network numbers for that IP address class.

## Slide 4
Class A
No of network = 28-2
No of host = 224-2
<number>
No of network = 216-2
No of host = 216-2
Class B
No of network = 224-2
No of host = 28-2 =254
Class C

## Slide 5: IP Address Classes Exercise
Address
Class
Network
Host
10.2.1.1
128.63.2.100
201.222.5.64
192.6.141.2
130.113.64.16
256.241.201.10
<number>
Notes: <number>
Layer 1 of 2:
Purpose: This exercise verifies that the students understand IP address classes, network numbers, and host numbers.
Give the students time to list the address class, network, and host number for each IP address in the table. Review the correct answers interactively.
The answers are given in the following figure.

## Slide 6: IP Address Classes Exercise Answers
Address
Class
Network
Host
10.2.1.1
128.63.2.100
201.222.5.64
192.6.141.2
130.113.64.16
256.241.201.10
A
B
C
C
B
Nonexistent
10.0.0.0
128.63.0.0
201.222.5.0
192.6.141.0
130.113.0.0
0.2.1.1
0.0.2.100
0.0.0.64
0.0.0.2
0.0.64.16
<number>
Notes: <number>
Layer 2 of 2:
Purpose: This answers to the exercise are given in the figure.
Note: Students can also find the answers to this exercise in the “Answers” appendix.

## Slide 7
10.15.13.2
172.16.2.160
200.50.40.5
X | Y | Z
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
1*X=X
0*X=0
<number>

## Slide 8: Default subnet
Notes: <number>
Purpose: This graphic explains how routers use addresses that have no subnet mask.
Emphasize: Explain how masking works at the bit level. Zero bits mask host information.
Note: This is an easy place to lose students. At this point, they need to learn several abstract mathematical concepts before we can show them how to lay out an IP-addressed network. To the novice, these techniques may seem unrelated, making the presentation confusing. To a more experienced audience, these techniques will be familiar.

## Slide 9: Subnet Mask with Subnets
Network number extended by eight bits
172.16.2.160/24
Notes: <number>
Slide 1 of 2
Purpose: This figure shows how the router determines an address when subnetting is used.
Emphasize: This example makes a Class B address space look like a collection of Class C address spaces.
Now the logical AND allows us to extract the subnet number as well as the assigned network number.
An exercise follows that tests the students’ understanding of subnet masks.

## Slide 10: Subnet Mask with Subnets (Cont.)
Network number extended by ten bits
172.16.2.160/26
Notes: <number>
Slide 2 of 2
Purpose: This figure shows how the router determines an address when subnetting is used.
Emphasize: This example is different from the previous example in that the the subnet and host are divided within an octet.
Transition: An exercise follows that tests the students’ understanding of subnet masks.

## Slide 11: Masks
In classful addressing, the mask for each block is implicit
  255.0.0.0/8
  255.255.0.0/16
  255.255.255.0/24
In classless addressing, we need the address and the mask to find the block the address belongs to

## Slide 12
<number>
Figure 5.2 Format of classless addressing address
An address in classless addressing usually has this format:
The n after the slash defines the number of bits that are the
same in every address in the block. So if n is 20, it means
the twenty leftmost bits are identical in each address.

## Slide 13: Prefix and Prefix Length
<number>
Two terms often used in classless addressing
  Prefix – another name for the common part of the address range (netid)
  Prefix length – the length of the prefix

## Slide 14
Table 5.1 Prefix lengths
The addresses in color are the default masks for classes A, B, and C.
Thus, classful addressing is a special case of classless addressing.

## Slide 15
What is the first address in the block if one of the addresses is 167.199.170.82/27?
Example 4 - Find first address
Address in binary: 10100111 11000111 10101010 01010010 Keep the left 27 bits: 10100111 11000111 10101010 01000000 Result in CIDR notation: 167.199.170.64/27
Solution The prefix length is 27, which means that we must keep the first 27 bits as is and change the remaining bits (5) to 0s. The following shows the process:

## Slide 16
What is the first address in the block if one of the addresses is 140.120.84.24/20?
Example 5 – Find first address Using binary
Solution Figure 5.3 shows the solution. The first, second, and fourth bytes are easy; for the third byte we keep the bits corresponding to the number of 1s in that group. The first address is 140.120.80.0/20.

## Slide 17
Figure 5.3 Example 5

## Slide 18
<number>
Find the first address in the block if one of the addresses is 140.120.84.24/20.
Example 6 – Find first address Another solution method

## Slide 19
Find the first address in the block if one of the addresses is 140.120.84.24/20.
Example 6 – Find first address Another solution method
Solution The first, second, and fourth bytes are as defined in the previous example. To find the third byte, we write 84 as the sum of powers of 2 and select only the leftmost 4 (m is 4) as shown in Figure 5.4. The first address is 140.120.80.0/20.

## Slide 20
Figure 5.4 Example 6

## Slide 21
Find the number of addresses in the block if one of the addresses is 140.120.84.24/20.
Example 7 - Number of addresses
Solution The prefix length is 20. The number of addresses in the block is 232−20 or 212 or 4096. Note that this is a large block with 4096 addresses.

## Slide 22
Find the last address in the block if one of the addresses is 140.120.84.24/20.
Example 8 - Find last address
Solution We found in the previous examples that the first address is 140.120.80.0/20 and the number of addresses is 4096. To find the last address, we need to add 4095 (4096 − 1) to the first address.

## Slide 23
To keep the format in dotted-decimal notation, we need to represent 4095 in base 256 (see Appendix B) and do the calculation in base 256. We write 4095 as 15.255. (256 divides into 4095 15 times with a remainder of 255.) We then add the first address to this number (in base 255) to obtain the last address as shown below:
Example 8 (Continued)
140 . 120 . 80 . 0 15 . 255 ------------------------- 140 . 120 . 95 . 255
The last address is 140.120.95.255/20.

## Slide 24: Alternate Method
Not crazy about base 256 arithmetic? Do it in binary.
.80.0 in binary is 01010000.00000000
4095 in binary is 1111 11111111
Add the two values:
  01011111.11111111
  This is .95.255

## Slide 25
Find the last address in the block if one of the addresses is 140.120.84.24/20.
Example 9 - find last address
Another method
Solution The mask has twenty 1s and twelve 0s. The complement of the mask has twenty 0s and twelve 1s. In other words, the mask complement is
00000000 00000000 00001111 11111111
or 0.0.15.255. We add the mask complement to the beginning address to find the last address.

## Slide 26
140 . 120 . 80 . 0 0 . 0 . 15 . 255 ---------------------------- 140 . 120 . 95 . 255
Example 9 (Continued)
We add the mask complement to the beginning address to find the last address.
The last address is 140.120.95.255/20.

## Slide 27
Find the block if one of the addresses is 190.87.140.202/29.
Example 10 - find the block
Solution We follow the procedure in the previous examples to find the first address, the number of addresses, and the last address. To find the first address, we notice that the mask (/29) has five 1s in the last byte. So we write the last byte as powers of 2 and retain only the leftmost five as shown below:

## Slide 28
202 ➡ 128 + 64 + 0 + 0 + 8 + 0 + 2 + 0
The leftmost 5 numbers are ➡ 128 + 64 + 0 + 0 + 8
The first address is 190.87.140.200/29
Example 10 (Continued)
The number of addresses is 232−29 or 8. To find the last address, we use the complement of the mask. The mask has twenty-nine 1s; the complement has three 1s. The complement is 0.0.0.7. If we add this to the first address, we get 190.87.140.207/29. In other words, the first address is 190.87.140.200/29, the last address is 190.87.140.207/20. There are only 8 addresses in this block.

## Slide 29: Subnet Mask Exercise Answers
Address
Subnet Mask
Class
Subnet
172.16.2.10
10.6.24.20
10.30.36.12
255.255.255.0
255.255.240.0
255.255.255.0
B
A
A
172.16.2.0
10.6.16.0
10.30.36.0
Notes: <number>
Layer 2 of 2:
Purpose: This answers to the exercise are given in the figure.
Note: Students can also find the answers to this exercise in the “Answers” appendix.

## Slide 30: Addressing Summary Example
16
172
2
160
10101100
00010000
10100000
00000010
Host
Mask
Subnet
Broadcast
Last
First
172.16.2.160
255.255.255.192
4
1
172.16.2.160/26
Notes: <number>
Layer 1 of 9:
Purpose: This example summarizes The IP addressing that was covered earlier in this chapter.
Emphasize:
In layer 1, convert the address to a binary host address.

## Slide 31: Addressing Summary Example
10101100
11111111
00010000
11111111
11111111
10100000
11000000
00000010
Host
Mask
Subnet
Broadcast
Last
First
172.16.2.160
255.255.255.192
1
2
16
172
2
160
172.16.2.160/26
Notes: <number>
Layer 2 of 9:
Emphasize: In layer 2, write the subnet mask in binary.

## Slide 32: Addressing Summary Example
10101100
11111111
00010000
11111111
11111111
10100000
11000000
00000010
Host
Mask
Subnet
Broadcast
Last
First
172.16.2.160
255.255.255.192
1
2
3
7
16
172
2
160
172.16.2.160/26
Notes: <number>
Layer 3 of 9:
Emphasize: In layer 3, draw a line after the recursive ones in the subnet mask.

## Slide 33: Addressing Summary Example
10101100
11111111
00010000
11111111
11111111
10100000
11000000
10000000
00000010
Host
Mask
Subnet
Broadcast
Last
First
172.16.2.160
255.255.255.192
1
2
3
4
16
172
2
160
172.16.2.160/26
Notes: <number>
Layer 4 of 9:
Emphasize: In layer 4, fill in zeros beyond the vertical line for the subnet.

## Slide 34: Addressing Summary Example
10101100
11111111
00010000
11111111
11111111
10100000
11000000
10000000
00000010
10111111
Host
Mask
Subnet
Broadcast
Last
First
172.16.2.160
255.255.255.192
1
2
3
4
5
6
16
172
2
160
172.16.2.160/26
Notes: <number>
Layer 5 of 9:
Emphasize: In layer 5, fill in ones beyond the vertical line for the broadcast address.

## Slide 35: Addressing Summary Example
10101100
11111111
00010000
11111111
11111111
10100000
11000000
10000000
00000010
10111111
10000001
Host
Mask
Subnet
Broadcast
Last
First
172.16.2.160
255.255.255.192
1
2
3
4
5
6
16
172
2
160
172.16.2.160/26
Notes: <number>
Layer 6 of 9:
Emphasize: In layer 6, fill in 0s beyond the vertical line except for the last bit. Make that bit a 1. This is the first usable host address.

## Slide 36: Addressing Summary Example
10101100
11111111
00010000
11111111
11111111
10100000
11000000
10000000
00000010
10111111
10000001
10111110
Host
Mask
Subnet
Broadcast
Last
First
172.16.2.160
255.255.255.192
1
2
3
4
5
6
7
16
172
2
160
172.16.2.160/26
Notes: <number>
Layer 7 of 9:
Emphasize: In layer 7, fill in 1s beyond the vertical line except for the last bit. Make that bit a 0. This is the last usable host address.

## Slide 37: Addressing Summary Example
10101100
11111111
10101100
00010000
11111111
00010000
11111111
00000010
10100000
11000000
10000000
00000010
10101100
00010000
00000010
10111111
10101100
00010000
00000010
10000001
10101100
00010000
00000010
10111110
Host
Mask
Subnet
Broadcast
Last
First
172.16.2.160
255.255.255.192
1
2
3
4
5
6
7
8
16
172
2
160
172.16.2.160/26
Notes: <number>
Layer 8 of 9:
Emphasize: In layer 8, copy the binary network and subnetwork address from the top row into the lower rows.

## Slide 38: Addressing Summary Example
10101100
11111111
10101100
00010000
11111111
00010000
11111111
00000010
10100000
11000000
10000000
00000010
10101100
00010000
00000010
10111111
10101100
00010000
00000010
10000001
10101100
00010000
00000010
10111110
Host
Mask
Subnet
Broadcast
Last
First
172.16.2.160
255.255.255.192
172.16.2.128
172.16.2.191
172.16.2.129
172.16.2.190
1
2
3
4
5
6
7
8
9
16
172
2
160
172.16.2.160/26
Notes: <number>
Layer 9 of 9:
Emphasize: In layer 9, convert binary back to dotted decimal.

## Slide 39
192.168.2.160& 192.168.2.200
Subnet mask 255.255.255.192
172.16.2.160
172.16.2.200
255.255.255.192
172.16.2.192
172.16.2.128
0
At the same
network connect
1
At different
network
Connect to gateway
Source address
Destination address
Subnet mask

## Slide 40: Class B Subnet Example
IP Host Address: 172.16.2.121
Subnet Mask: 255.255.255.0
Subnet Address = 172.16.2.0
Host Addresses = 172.16.2.1–172.16.2.254
Broadcast Address = 172.16.2.255
Eight bits of subnetting
Network
Subnet
Host
10101100
00010000
00000010
11111111
172.16.2.121:
255.255.255.0:
10101100
11111111
Subnet:
10101100
00010000
00010000
11111111
00000010
00000010
11111111
01111001
00000000
00000000
Broadcast:
Network
172.16.2.121/24
Notes: <number>
Purpose: This figure shows an example of a Class B network with a subnet.

## Slide 41: Class C Subnet Planning Example
11111000
IP Host Address: 192.168.5.121
Subnet Mask: 255.255.255.248
Network
Subnet
Host
192.168.5.121:
11000000
11111111
Subnet:
11000000
10101000
10101000
11111111
00000101
00000101
11111111
01111001
01111000
255.255.255.248:
Subnet Address = 192.168.5.120
Host Addresses = 192.168.5.121–192.168.5.126
Broadcast Address = 192.168.5.127
Five Bits of Subnetting
Broadcast:
Network
Network
11000000
10101000
00000101
01111111
192.168.5.121/29
Notes: <number>
Purpose: This figure shows an example of a Class C network with a subnet.
Emphasize: Contrast the Class C network subnet mask with the previous Class B example.

## Slide 42: Broadcast Addresses Exercise
Address
Class
Subnet
Broadcast
201.222.10.60
255.255.255.248
Subnet Mask
15.16.193.6
255.255.248.0
128.16.32.13
255.255.255.252
153.50.6.27
255.255.255.128
Notes: <number>
Layer 1 of 2:
Purpose: Have the students calculate the subnet numbers and the broadcast address for each subnet from the given IP addresses and subnet masks.

## Slide 43: Broadcast Addresses Exercise Answers
153.50.6.127
Address
Class
Subnet
Broadcast
201.222.10.60
255.255.255.248
C
201.222.10.63
201.222.10.56
Subnet Mask
15.16.193.6
255.255.248.0
A
15.16.199.255
15.16.192.0
128.16.32.13
255.255.255.252
B
128.16.32.15
128.16.32.12
153.50.6.27
255.255.255.128
B
153.50.6.0
Notes: <number>
Layer 2 of 2:
Purpose: This answers to the exercise are given in the figure.
Note: Students can also find the answers to this exercise in the “Answers” appendix.

## Slide 44: design
192.168.10.0/24 5 Dept, 25 user
First note 192.168.10.0 class c
Default mask = 255.255.255.0
No of network = 2^n-2 >= 5 ……….n=3
For check
No of host = 2^5 – 2 = 30 > 25
Ok
The subnet mask is 255.255.255.11100000
255.255.255.224
<number>

## Slide 45
192
255
192
168
255
168
255
5
00100000
11100000
00100000
5
192
168
5
00111111
01000000
01011111
Host
Mask
Subnet
Broadcast
192.168.5.32
255.255.255.224
192.168.5.32
192.168.5.63
192.168.5.64
192.168.5.95
192
5
0
192
192
168
168
5
5
01100000
01111111
192.168.5.96
192.168.5.127
192
192
168
168
5
5
Subnet
Subnet
Broadcast
Broadcast
168
<number>
192.168.5.32/27
Notes: <number>
Layer 9 of 9:
Emphasize: In layer 9, convert binary back to dotted decimal.

## Slide 46
192
255
168
255
255
00000000
11100000
5
Host
Mask
192.168.5.0
255.255.255.224
192
5
0
Factor = 2^5 = 32
192.168.5.0
+32
192.168.5.32
+32
192.168.5.64
+32
192.168.5.96
+23
192.168.5.128
168
<number>
192.168.5.32/27