## Slide 1: IP datagram fields cont.
The total length field defines the total length of the datagram Including the header.
Total length field is 16 bits, or 65,535 bytes. Of which 20 to 60 bytes are the header.

## Slide 2: IP datagram fields cont.
Identification, Flags, and Fragmentation offset are all used to perform fragmentation.
Time to Live - 8-bit field, so Time to Live can be set to 255.
As it passes thru a router, the router decrements the counter. When counter hits 0, the datagram is deleted (and ICMP sends an error message back to the source).

## Slide 3: IP datagram fields cont.
The Protocol field (8 bits) identifies the upper layer protocol that is using IP for transmission of its data.

## Slide 4: IP datagram fields cont.
These are some common values that are used in the Protocol field

## Slide 5: IP datagram fields cont.
Header Checksum: Over the IP header only. Each 16-bit separated, then all added using one’s complement. Then taking the one’s complement of the result. Answer should be 1s.
  Upon checksum error, datagram is dropped and no indication is sent back.
Options:
  Security and handling restrictions

## Slide 6: IP Addressing
IP Address
  Logical address used in TCP/IP networking
  Unique 32-bit number
    Divided into four groups of octets (8-bit bytes) that are separated by periods.
    E.g., 217.29.240.5 (www.asu.edu.jo)
Total: 232 = 4,294,967,296

## Slide 7: IP Addressing cont.
Loopback address
  IP address reserved for communicating from a node to itself (localhost)
  Value of the loopback address is always 127.0.0.1
Internet Corporation for Assigned Names and Numbers (ICANN)
  Non-profit organization to maintain and assign IP addresses

## Slide 8: Why IP Addresses?
172.18.0.2
172.18.0.1
172.17.0.2
172.17.0.1
172.16.0.2
10.13.0.0
192.168.1.0
10.13.0.1
192.168.1.1
172.16.0.1

## Slide 9: Why IP Addresses? Cont.
Unique addressing allows communication between end stations
  Unicast (one-to-one)
  Broadcast (one-to-all)
  Multicast (one-to-many)
Path choice is based on location
Location is represented by an address

## Slide 10: IP Addresses Classful Addressing
Class A:
Class B:
Class C:
Class D: Multicast
Class E: Research
Network
Host
Host
Host
Network
Network
Host
Host
Network
Network
Network
Host
8 bits
8 bits
8 bits
8 bits

## Slide 11: IP

## Slide 12: 4.2 CLASSFUL ADDRESSING CLASSFUL ADDRESSING
IP addresses, when started a few decades ago, used the concept of classes. This architecture is called classful addressing. In the mid-1990s, a new architecture, called classless addressing, was introduced and will eventually supersede the original architecture. However, part of the Internet is still using classful addressing, but the migration is very fast.

## Slide 13: Address Space
Class A addresses cover ½ the address space!!
Millions of class A addresses are wasted!

## Slide 14: Addresses per class