## Slide 1: Longest Mask Matching
What happens if one of the organizations is not geographically close to the others, like in Figure 6.16.
No problem, as long as the routing table is sorted longest mask to shortest mask.

## Slide 2
Figure 6.16 Longest mask matching

## Slide 3
As an example of hierarchical routing, let us consider Figure 6.17. A regional ISP is granted 16384 addresses starting from 120.14.64.0. The regional ISP has decided to divide this block into four subblocks, each with 4096 addresses. Three of these subblocks are assigned to three local ISPs, the second subblock is reserved for future use. Note that the mask for each block is /20 because the original block with mask /18 is divided into 4 blocks.
Example 12
See Next Slide

## Slide 4
Figure 6.17 Hierarchical routing with ISPs

## Slide 5
The first local ISP has divided its assigned subblock into 8 smaller blocks and assigned each to a small ISP. Each small ISP provides services to 128 households (H001 to H128), each using four addresses. Note that the mask for each small ISP is now /23 because the block is further divided into 8 blocks. Each household has a mask of /30, because a household has only 4 addresses (232−30 is 4).
The second local ISP has divided its block into 4 blocks and has assigned the addresses to 4 large organizations (LOrg01 to LOrg04). Note that each large organization has 1024 addresses and the mask is /22.
Example 12 (Continued)
See Next Slide

## Slide 6
The third local ISP has divided its block into 16 blocks and assigned each block to a small organization (SOrg01 to SOrg15). Each small organization has 256 addresses and the mask is /24.
There is a sense of hierarchy in this configuration. All routers in the Internet send a packet with destination address 120.14.64.0 to 120.14.127.255 to the regional ISP. The regional ISP sends every packet with destination address 120.14.64.0 to 120.14.79.255 to Local ISP1. Local ISP1 sends every packet with destination address 120.14.64.0 to 120.14.64.3 to H001.
Example 12 (Continued)

## Slide 7
6.3 ROUTING
Routing deals with the issues of creating and maintaining routing tables.
The topics discussed in this section include:
Static Versus Dynamic Routing Tables
Routing Table

## Slide 8
Figure 6.18 Common fields in a routing table

## Slide 9
One utility that can be used to find the contents of a routing table for a host or router is netstat in UNIX or LINUX. The following shows the listing of the contents of the default server. We have used two options, r and n. The option r indicates that we are interested in the routing table and the option n indicates that we are looking for numeric addresses. Note that this is a routing table for a host, not a router. Although we discussed the routing table for a router throughout the chapter, a host also needs a routing table.
Example 13
See Next Slide

## Slide 10
$ netstat -rn Kernel IP routing table
Destination Gateway Mask Flags Iface
153.18.16.0 0.0.0.0 255.255.240.0 U eth0
127.0.0.0 0.0.0.0 255.0.0.0 U lo
0.0.0.0 153.18.31. 254 0.0.0.0 UG eth0.
Example 13 (continued)
See Next Slide