## Slide 1
2017-2018
Computer Networks Protocols

## Slide 2
Lecture No.1: Introduction
Network Architecture
A set of layers and protocols is called the network architecture.
Protocol Hierarchies
 Networks are organized as layers to reduce design complexity.
 Each layer offers services to the higher layers. Between adjacent layers is an interface.
Services | Interface | Primitives
connection oriented and connectionless. | defines which primitives and services the lower layer will offer to the upper layer. | operations such as request, indicate, response, confirm.
Design Issues for the Layers(functions)
1. Mechanism for connection establishment
2. Rules for data transfer
3. Error control
4. Fast sender swamping a slow receiver
5. Routing in the case of multiple paths
Network Protocols
· Protocol: is a format order of messages sent and received among the net entities and action taken on msgs
transmission receipt.
· Protocol process :
1. The format or structure of the message
2. The process by which networking devices share information about pathways with other networks
3. How and when error and system messages are passed between devices
4. The setup and termination of data transfer sessions
Layering In Networked Computing
· OSI Model (open system interconnection)
· TCP/IP Model
Why a layered model?
1. Breaks down communication into smaller, simpler parts.
2. Easier to teach communication process.
3. Allows different hardware and software to work together.
4. Reduces complexity
The OSI model

## Slide 3
The Open Systems Interconnection is the model developed by the International Standards Organization.
-
helps us understand how data gets from one user’s computer to another.
-It aids to provide an organized structure for hardware and software developers to follow.
Why use a reference model?
– Serves as an outline of rules for how protocols can be used to allow communication between computers.
– Each layer has its own function and provides support to other layers.
Benefits(Advantage) | Negative Aspect (disadvantage)
· Interconnection of different systems (open) · Not limited to a single vendor solution | · Systems might be less secure · Systems might be less stable
Layer Main Topics

## Slide 4
Physical Layer | · · · · · · | Transmission mediums (transmit bits over medium) Encoding Modulation Repeaters Hubs (multi-port repeater) To provide mechanical and electrical specification
Data Link Layer | · · · · · · · | Error detection and correction methods Hop to hop delivery Flow control Frame format IEEE LAN standards Bridges & Switches (multi-port bridges) physical addressing(MAC Address)
Network Layer | · · · · · | Internetworking Controls the operation of the subnet. Routing algorithms(Routing packets from source to destination) Internet Protocol (IP) addressing (Logical addressing) Routers
Transport Layer | · · · · · · · | Connection-oriented and connectionless services Provide reliable process to process message delivery & error recovery Transmission Control Protocol (TCP) User Datagram Protocol (UDP) Provides additional Quality of Service. Port address End-to-end flow control.
Session Layer | · · · · | Allows users on different machines to establish sessions (dialogue) between them. managing dialogue control. Token management. Synchronization.
Presentation Layer | · · · · | Concerned with the syntax and semantics of the information. Preserves the meaning of the information. Data compression. Data encryption.
Application Layer | · · · | Provides protocols that are commonly needed. To allow access to network resource (FTP), (HTTP), (SMTP), (SNMP),(NFS),(Telnet)
SERVICES
Connection-Oriented | Connectionless
before data is sent, the service from the sending computer must establish a connection with the receiving computer. | data can be sent at any time by the service from the sending computer.

## Slide 5
OSI(Open System Interconnection) | TCP/IP(Transmission Control Protocol / Internet Protocol)
1. OSI provides layer functioning and also defines functions of all the layers. | 1. TCP/IP model is more based on protocols and protocols are not flexible with other layers.
2. OSI model has a separate presentation layer | 2. TCP/IP does not have a separate presentation layer
3. OSI is a general model. | 3. TCP/IP model cannot be used in any other application.
4. Network layer of OSI model provide both connection oriented and connectionless service. | 4. The Network layer in TCP/IP model provides connectionless service.
5. OSI model has a problem of fitting the protocols in the model | 5. TCP/IP model does not fit any protocol
6. Protocols are hidden in OSI model and are easily replaced as the technology changes. | 6. In TCP/IP replacing protocol is not easy.
7. OSI model defines services, interfaces and protocols very clearly and makes clear distinction between them. | 7. In TCP/IP it is not clearly separated its services, interfaces and protocols.
8. It has 7 layers | 8. It has 4 layers

## Slide 6
Data Encapsulation
·Each layer contains a Protocol Data Unit (PDU)
 PDU’s are used for peer-to-peer contact between corresponding layers.
The Layer | Shape of data (PDU)
top three layers | Data
Transport layer | Segment
Network layer | packets
Data Link layer | frames
Physical layer | bits
4 layers of the TCP/IP model
·Layer 4: Application
·Layer 3: Transport
·Layer 2: Internet
·Layer 1: Network access
It is important to note that some of the layers in the TCP/IP model have the same
name as layers in the OSI model. Do not confuse the layers of the two models.
Data Encapsulation In TCP/IP
 Outgoing data is packaged and identified for delivery to the layer underneath
 PDU – Packet Data Unit – the “envelop” information attached to a packet at a particular
TCP/IP protocol e.g. header and trailer
 Header (Identifies the protocol in use, the sender and intended recipient)
 Trailer (or packet trailer) (Provides data integrity checks for the payload)

## Slide 7
Data Formats
Encapsulation (TCP/IP)
Encapsulation example: E-mail

## Slide 8
TCP/IP protocol stack
TCP/IP Reference Model
What is a socket?
 An interface between application and network( each application create socket)
 Socket(Protocolfamily, type-of-communication, specific- protocol);
 The socket type dictates the style of communication
reliable vs. best effort
connection-oriented vs. connectionless
Q/Explain the delivery of data in Layered model?
Type of delivery | Layer | Shape of data | Type of addressing
End to End | Transport | Segment | Port (socket)
Source To Destination | Network | Packet | Logical (IP)
Node to Node | Data Link | Frame | Physical(MAC)