## Slide 2
Computer Networks Protocols
Lecture No.2: Physical & Data link layer
PHYSICAL LAYER
SONET\SDH Networks
 SONET\SDH, that is used as a transport network to carry loads from other WANs.
SDH(Synchronous Digital Hierarchy) |  | SONET(Synchronous Optical Network)
 Is European standard network. |  | Is American standard network.
 Is a standard developed by ITU-T. |  | Is a standard developed by ANSI for fiber-optic networks.
 Define a hierarchy of signals called synchronous transfer modules (STMs( |  | Define a hierarchy of signals called synchronous transport signals (STSs( where each STS level (STS-1 to STS-192) supports a certain data rate.

## Slide 3
BLUETOOTH
 Bluetooth is a wireless LAN technology designed to connect devices of different functions
such as telephones, notebooks, computers (desktop and laptop), cameras, printers, and even
coffee makers when they are at a short distance from each other.
Architecture of Bluetooth:
 Bluetooth defines two types of networks: piconet and scatternet.
 A Bluetooth network is called a piconet, or a small net. A piconet can have up to eight
stations, one of which is called the primary; the rest are called secondaries.
Piconet Network
Scatternet Network

## Slide 4
Data Link Layer
1.Elementary Data Link Protocols
An Unrestricted Simplex Protocol (SP) | one direction transmitted data
A Simplex Stop-and-Wait Protocol(SWP) | flooding control
A Simplex Protocol for a Noisy Channel(SPN) | limit send and receive between sender and receiver, capacities are limited
2. Sliding Window Protocols
A One-Bit Sliding Window Protocol(SWP) | 1- assign variable 2- define frame 3- accept frame
A Protocol Using Go Back N protocol | Discarding &Buffering
A Protocol Using Selective Repeat (SRP) | accept and buffer delay and effected frame) without ACK
Go Back N Protocol
Selective repeat Protocol SRP

## Slide 5
PPP – Point to Point Protocol
 Carry network data of any network layer protocol at the same time
 Error detection (no correction)
 has a very simple mechanism for error control( A CRC field is used to detect errors )
 Does not provide flow control
 Connection life, signal link, negotiator
Address Resolution Protocol (ARP)
·The delivery of a packet to a host or a router requires two levels of addressing: logical and physical.
–ARP Maps IP addresses to MAC addresses
–ARP Request is a broadcast but ARP reply is Unicast .
–ARP tables contain the MAC and IP addresses of other devices on the network
ARP operation:

## Slide 6
Layer 2 Tunneling Protocol (L2TP)
 is an extension of the Point-to-Point Tunneling Protocol (PPTP).
 used by an Internet service provider (ISP) to enable the operation of a virtual private
network (VPN) over the Internet.
 VPN The goal of a Virtual Private Network (VPN) is to provide private communications
within the public Internet Infrastructure
Why is there a need for VPN?
 Internet has insufficient security mechanisms
 IP packets are not authenticated or encrypted
 Users with access to network can read content of IP traffic
Transition from IPv4 to IPv6
not all routers can be upgraded simultaneously
tunneling: IPv6 datagram carried as payload in IPv4 datagram among IPv4 routers
Tunneling

## Slide 7
Spanning Tree Protocol(STP)
Redundancy in a network, such as that shown in Figure below, is desirable so that communication
can still take place if a link or device fails.
For example, if switch X in this figure stopped functioning, devices A and B could still communicate
through switch Y. However, in a switched network, redundancy can cause problems.
There are 3 problems:
1. occurs if a broadcast frame is sent on the network((broadcast storm).
2. that can occur in redundant topologies is that devices can receive multiple copies of the same
frame.
3. that can occur in a redundant situation is within the switch itself—the MAC address table can
change rapidly and contain wrong information.
To overcome these problems:
you must have a way to logically disable part of the redundant network for regular traffic while
maintaining redundancy for the case when an error occurs. STP does just that.

## Slide 8
Access Method: CSMA/CD
 Whenever multiple users have unregulated access to a single line, there is a danger of signals
overlapping and destroying each other. Such overlaps, which turn the signals into unusable
noise, are called collisions.
 As traffic increases on a multiple access link, so do collisions. A LAN therefore needs a
mechanism to coordinate traffic, minimize the number of collisions that occur, and
maximize the number of frames that are delivered successfully.
 The access mechanism used in an Ethernet is called carrier sense multiple access with
collision detection (CSMA/CD, standardized in IEEE 802.3).
 CSNIA/CD is the result of an evolution from multiple access (MA) to carrier sense multiple
access (CSMA), and finally, to carrier sense multiple access with collision detection
(CSMA/CD).
·Carrier Sense: when a station in an Ethernet network has data to transmit ,it first see the network if it
is use by other stations this is carrier sense .under three case of persistence strategy
Non-persistence | senses the line if it is idle it sends immediately if the line busy ,it waits a random time then sense the line again this method reduce the chance of collision but it also reduced network efficiency.
1-persistence | after the station finds the line idle it sends its data immediately (with probability 1) this method increase the chance of collision.
p-persistence | after the station finds the line idle it may transmit or no. here the probability of sending is defined by P and probability of refusing is (1-P) for example if p=0.3 then station sends with 30% of the time and refusing 70% of the time . The station generates a random number between 1 and 100 if the number generated is less than 30 the station sends its data else it waits one slot time before sensing the medium again this method reduces the chance of collision and increasing network efficiency.
.Jam signal : when system detected a collision it immediately stop transmitting data and starts sending
this signal any system received packet must discard this packet and should not attempt to transmit any
data until network has cleared.

## Slide 10
Cyclical Redundancy Check (CRC)
The most powerful redundancy technique, unlike the VRC and LRC, CRC is based on binary
division.

## Slide 11
Checksum
The error detection method used by the higher layer protocols. Like other methods, it depends
on the concept of redundancy.