## Slide 2
Computer Networks Protocols
Lecture No.4:Network Layer Part 2
Routing Protocols
 A routing protocol is a combination of rules and a procedure that lets routers in the internet
inform each other of changes.
 Routing metric: a method by which routing algorithms determines that one route is better than
another route ,Metric may be(hop count, bandwidth,delay,load)
Interior Versus Exterior Routing Protocols
An autonomous system (AS), also known as a domain, is a collection of routers that are under a
common administration, such as a company’s internal network or an Internet service provider’s
(ISP’s) network.
Because the Internet is based on the AS concept, two types of routing protocols are required:
Interior gateway protocols (IGP) | Exterior gateway protocols (EGP)
Intra-AS (inside an AS) routing protocols. | Inter-AS (between autonomous systems) routing protocols.
Examples of IGPs include: Routing Information Protocol (RIP) RIP version 2 (RIPv2), Open Shortest Path First (OSPF), and Enhanced Interior Gateway Routing Protocol (EIGRP). | Border Gateway Protocol (BGP) is the only widely used EGP protocol on the Internet. BGP version 4 (BGP-4) is considered the acceptable version of BGP on the Internet.
use less-complicated metrics to ease configuration and speed up the decisions about best routing paths for faster convergence | Slower to converge and more complex to configure.

## Slide 3
Popular routing protocols
RIP ( Routing Information Protocol)
 RIP is a routing protocol for exchanging routing table information between routers.
 It is a very simple protocol based on distance vector routing.
 simple intra-domain protocol
 Uses hop count as a path selection metric. (RIP prevents routing loops by implementing a
limit on the number of hops allowed in a path from the source to a destination. The maximum
number of hops allowed for RIP is 15. This hop limit, however, also limits the size of networks
that RIP can support, a hop count of 16 is considered an infinite distance, in other words the
route is considered unreachable).
 Three types of timers.

## Slide 4
Timers
Routing-update timer (periodic timer)
 The periodic timer controls the advertising of regular update messages.
 By default, routers send updates every 30 seconds.
Route timeout (Expiration Timer)
 If there is a problem on an internet and no update is received within the allotted 180 s, the
route is considered expired and the hop count of the route is set to 16, which means the
destination is unreachable.
Route-flush timer (Garbage Collection Timer )
 After the route timeout expires, the route-flush timer eventually expires, deleting the route
from the table.
Drawbacks
 RIP has slow convergence and count to infinity problems
 The hop count cannot exceed 15, or routes will be dropped.

## Slide 6
OSPF (Open Shortest Path First)
 It uses a link state routing algorithm and falls into the group of interior routing protocols,
operating within a single autonomous system (AS).
 topology map at each node
 route computation using Dijkstra’s algorithm
 OSPF is perhaps the most widely used interior gateway protocol (IGP) in large enterprise
networks.'
 The metric of OSPF is the cost of sending packets across a certain interface
 “open”: publicly available
 "security": all OSPF messages authenticated (to prevent malicious intrusion)
 Hierarchical OSPF in large domains.
Hierarchical OSPF
 Two-level hierarchy: local area, backbone.
 Link-state advertisements only in area
 Each node has detailed area topology; only know direction (shortest path) to nets in other
areas.
 Area border routers: “summarize” distances to nets in own area, advertise to other Area
Border routers.
 Backbone routers: run OSPF routing limited to backbone.
 Boundary routers: connect to other AS’s.
OSPF is superior to RIP in all aspects, including the following:
 It converges much faster.
 It supports hierarchical structures.
 It has improved metric calculation for best path selection.
 It does not have hop-count limitations

## Slide 7
 At its inception, OSPF supported the largest networks.
 Compare to RIP, OSPF has no limitation due to hops (RIP has a limit of 15 hops so any
network with more than 15 hops cannot be achieved by RIP.
EIGRP
 EIGRP is a protocol for routing IPv4 and IPv6 .
 EIGRP, however, is a hybrid routing protocol—it is a distance vector protocol with
additional link-state protocol features.
 Uses triggered updates (EIGRP has no periodic updates).
 provide fast convergence to minimize network traffic.
 uses the minimum bandwidth on the path of the destination network, and calculate a route
from the total delay metrics.
Border Gateway Protocol(BGP )
· Inter-domain routing protocol for routing between autonomous systems ( holds the Internet
together)
· BGP is neither a link state, nor a distance vector protocol. Routing messages in BGP
contain complete routes.
· Network administrators can specify routing policies(BGP supports flexibility -- paths could
be chosen by a provider based on a policy.
· Network administrators can specify routing policies.
· BGP’s goal is to find any path (not an optimal one).
Internal and external BGP sessions
 | iBGP | eBGP | 
 | used to connect different routers have same AS(same company) |  | used to connect different routers have different AS(different company)
 | propagate reach ability information to all AS-internal routers. |  | obtain subnet reach ability information from neighboring ASs.

## Slide 8
Example: when AS3 advertises a prefix to AS1:
–AS3 promises it will forward datagrams towards that prefix
–AS3 can aggregate prefixes in its advertisement
BGP basics: distributing path information
Using eBGP session between 3a and 1c, AS3 sends prefix reachability info to AS1.
 1c can then use iBGP do distribute new prefix info to all routers in AS1
 1b can then re-advertise new reachability info to AS2 over 1b-to-2a eBGP session
 When router learns of new prefix, it creates entry for prefix in its forwarding table.
BGP route selection
Router may learn about more than 1 route to destination AS, selects route based on:
1. Local preference value attribute: policy decision
2. Shortest AS-PATH
3. Closest NEXT-HOP router.
4. Additional criteria
BGP Messages
BGP messages exchanged between peers over TCP connection, BGP has four types of messages
 OPEN: Establish a connection with a BGP peer
 UPDATE -- advertise or withdraw routes to a destination
 KEEPALIVE: Inform a peer that the sender is still alive but has no information to send.
 NOTIFICATION: Notify that errors are detected, also used to close connection